## Slide 1: Computer Organization & Assembly Language
Lecture 1

## Slide 2: Outline
About this Course
Basic Structure of Computer
What is Computer Organization?
About Assembly Language

## Slide 3: Course Objectives
To learn the organization of computer hardware components.
To gain knowledge about the internal architecture and working of microprocessors.
To understand working of memory devices, interrupt controllers and I/O devices.
Develop skills to analyze and optimize performance at the machine level.
To understand syntax, semantics, and structure of assembly language.
Notes: Microprocessor -> CPU (processor) on a single chip

## Slide 4: Course Contents
Computer Architecture
Assembly Language Fundamentals
Data Representation
Memory Hierarchy
Input/Output Systems

## Slide 5: Real World Applications
Embedded Systems
  Home Automation (Smart Homes)
  Automotive Systems (Vehicles)
Missile Guidance Systems
Home Appliances
Medical Devices
Consumer Electronics (Smartphones)
Robotics

## Slide 6: Why Assembly Language?
Direct Hardware Control
Performance Optimization
Understanding Computer Architecture
Embedded Systems Expertise (low cost)
Real-Time Processing
Foundation for Other Languages

## Slide 7: Structure
Structure is the way in which components relate to each other

## Slide 8: Difference in Peripherals & Communication Lines
When data is received from or delivered by a device that is directly connected to the computer, process is called Input-Output (I/O).
When data are moved over longer distance, to or from a remote device, the process is known as Data Communication.

## Slide 9: Computer Architecture
Computer Architecture refers to those attributes of a system visible to a programmer
  Those attributes that have direct impact on logical execution of a program.
Architectural attributes include:
  the instruction set,
  no. of bits used to represent various data types (numbers, characters etc),
  I/O mechanisms and technology for addressing memory.
Example: Architectural design issue whether a computer will have multiple instruction or not.
Notes: Architecture = Logical aspects
Explain the terms underlined

## Slide 10: Computer Architecture
Processor-Memory-I/O Model
Components
  CPU
  Memory
  I/O Devices
Data Flow
System Interconnect
Basic Instruction Cycle (Fetch-> Execute)
Notes: Architecture = Logical aspects
Explain the terms underlined

## Slide 11: Structure - Top Level
Computer
Main
Memory
Input
Output
Systems
Interconnection
Peripherals
Communication
lines
Central
Processing
Unit
Computer

## Slide 12: Structure - The CPU
Computer
Arithmetic
and
Login Unit
Control
Unit
Internal CPU
Interconnection
Registers
CPU
I/O
Memory
System
Bus
CPU

## Slide 13: What is a Bus?
A communication pathway connecting two or more devices
Often grouped
  A number of channels in one bus
  e.g. 32 bit data bus is 32 separate single bit channels
CPU
Memory
I/O
Address Bus
Control Bus
Data Bus

## Slide 14: Data Bus
Carries data
  Remember that there is no difference between “data” and “instruction” at this level
Width is a key determinant of performance
  8, 16, 32, 64 bit
  Bidirectional

## Slide 15: Address bus
Identify the source or destination of data
  e.g. CPU needs to read an instruction (data) from a given location in memory
Bus width determines maximum memory capacity of system
  e.g. 8080 has 16 bit address bus giving 64k address space

## Slide 16: Control Bus
Control and timing information
  Memory read/write signal
  Interrupt request
  Timing signals

## Slide 17: Programming Languages
High-Level Languages (HLL)
Assembly Language
Machine Language

## Slide 18: High-Level Language
Allow programmers to write programs that look more like natural language.
Examples: C++, Java, C#, .NET etc
A program called Compiler is needed to translate a high-level language program into machine code.
Each statement usually translates into multiple machine language instructions.

## Slide 19: Machine Language
The "native" language of the computer
Numeric instructions and operands that can be stored in memory and are directly executed by computer system.
Each ML instruction contains an op code (operation code) and zero or more operands.
Examples:
Opcode Operand Meaning
-------------------------------------------------
40 increment the AX register
05 0005 add 0005 to AX

## Slide 20: Assembly Language
Use instruction mnemonics that have one-to-one correspondence with machine language.
An instruction is a symbolic representation of a single machine instruction
Consists of:
  label always optional
  mnemonic always required
  operand(s) required by some instructions
  comment always optional

## Slide 21
Sample Program

## Slide 22: CPU
Brain of Computer; controls all operations
  Uses Memory Circuits to store information
  Uses I/O Circuits to communicate with I/O Devices
Executes programs stored in memory
  System programs
  Application programs
Instruction Set: Instructions performed by CPU
Two main components:
  Execution Unit (EU)
  Bus Interface Unit (BIU)

## Slide 23: Intel 8086 Microprocessor
Introduced in 1978
One of the first 16-bit microprocessors.
It laid the foundation for the x86 architecture, which remains prevalent today.

## Slide 24: Execution Unit (EU)
Purpose: Execute instructions
Contains ALU (Arithmetic & Logic Unit)
  To perform arithmetic (+, -, x,/) and logic (AND, OR, NOT) operations.
The data for the operations are stored in circuits called Registers.
A register is like a memory location except that it is referred by a name not a number (address).
EU uses registers for:
  Storing data.
  Holding operands for ALU
  To reflect result of a computation – FLAG register
Notes: Register details covered in later slides

## Slide 25: Bus Interface Unit (BIU)
Facilitates communication between the EU and the memory or I/O circuits.
Responsible for transmitting address, data and control signals on the buses.

## Slide 26
Intel 8086 Microprocessor Organization

## Slide 27: Bits, Bytes and Double words
Each 1 or 0 is called a bit.
Group of 8 bits = Byte
Group of 16 bits = Word
Group of 32 bits = Double words

## Slide 28: Registers
Registers are high-speed storage locations inside the microprocessor.
Designed to be accessed at much higher speed than conventional memory.
Registers are classified according to the functions they perform.
General Types of Registers:
  Data Registers: To hold data for an operation.
  Address Registers: To hold the address of an instruction or data.
  Status/Flag Register: keeps the current status of the processor or result of an arithmetic operation.

## Slide 29: 8086 Internal registers 16 bits (2 bytes each)
AX, BX, CX and DX are two
bytes wide and each byte can
be accessed separately
These registers are used as
memory pointers.
Segment registers are used
as base address for a segment
6 status; 3 control ; 7 unused

## Slide 30: General Purpose/Data Registers
Following four registers are available to the programmer for general data manipulation:
AX (Accumulator): Used in arithmetic, logic and data transfer instructions. Also required in multiplication, division and input/output operations.
BX (Base): It can hold a memory address that points to a variable.
CX (Counter): Act as a counter for repeating or looping instructions. These instructions automatically repeat and decrement CX and quit when equals to 0.
DX (Data): It has a special role in multiply and divide operations. Also used in input/output operations.

## Slide 31: Segment Registers
Store addresses of instruction and data in memory.
These values are used by the processor to access memory locations.
CS (Code): Defines the starting address of the section of memory holding code.
DS (Data): Defines the section of memory that holds most of the data used by programs.
ES (Extra): This is an additional data segment that is used by some of the string instructions.
SS (Stack): It defines the area of the memory used for stack

## Slide 32: Pointers and Index Registers
IP - instruction pointer: Always points to next instruction to be executed. IP register always works together with CS segment register.
SI - source index register: Can be used for pointer addressing of data. Works together with DS segment register.
DI - destination index register: Can be used for pointer addressing of data. Works together with ES segment register.
BP - base pointer: Primarily used to access parameters passed via the stack. Works together with SS segment register.
SP – stack pointer: Always points to top item on the stack. Works together with SS segment register.

## Slide 33: Thank You