## Slide 1: Computer Organization & Assembly Language
Revision: Data Representation

## Slide 2: Number System
Any number system using a range of digits that represents A specific number. The most common numbering systems are decimal, binary, octal, and hexadecimal.
Numbers are important to computers
  Represent information precisely
  Can be processed
For example:
  To represent yes or no: use 0 for no and 1 for yes

## Slide 3: Decimal Number System

## Slide 4: Binary Number System

## Slide 5: Hexadecimal Number System

## Slide 6: Conversion Between Number Systems
Converting Hexadecimal to Decimal
Multiply each digit of the hexadecimal number from right to left with its corresponding power of 16.
Convert the Hexadecimal number 82ADh to decimal number.
0x82AD (memory addressing)

## Slide 7: Conversion Between Number Systems
Converting Binary to Decimal
Multiply each digit of the binary number from right to left with its corresponding power of 2.
Convert the Binary number 11101 to decimal number.

## Slide 8: Conversion Between Number Systems
Converting Decimal to Binary
Divide the decimal number by 2.
Take the remainder and record it on the side.
REPEAT UNTIL the decimal number cannot be divided into anymore.

## Slide 9: Conversion Between Number Systems
Converting Decimal to Hexadecimal
Divide the decimal number by 16.
Take the remainder and record it on the side.
REPEAT UNTIL the decimal number cannot be divided into anymore.

## Slide 10: Binary Arithmetic Operations
Addition
Like decimal numbers, two numbers can be added by adding each pair of digits together with carry propagation.
11001
+ 10011
101100
647
+ 537
1184
Binary Addition
Decimal Addition

## Slide 11: Binary Arithmetic Operations
Subtraction
Two numbers can be subtracted by subtracting each pair of digits together with borrowing, where needed.
11001
- 10011
00110
627
- 537
090
Binary Subtraction
Decimal Subtraction

## Slide 12: Hexadecimal Arithmetic Operations
Hex Addition
Like decimal numbers, two numbers can be added by adding each pair of digits together with carry propagation.
5B39
+ 7AF4
D62D
Hexadecimal Addition

## Slide 13: HexaDecimal Arithmetic Operations
Hex Subtraction
Two numbers can be subtracted by subtracting each pair of digits together with borrowing, where needed.
D26F
- BA94
17DB
Hexadecimal Subtraction

## Slide 14: MSB and LSB
In computing, the most significant bit (MSB) is the bit position in a binary number having the greatest value. The MSB is sometimes referred to as the left-most bit.
In computing, the least significant bit (LSB) is the bit position in a binary integer giving the units value, that is, determining whether the number is even or odd. The LSB is sometimes referred to as the right-most bit.

## Slide 15: Unsigned Integers
An unsigned integer is an integer that represents a magnitude, so it is never negative.
Unsigned integers are appropriate for representing quantities that can never be negative.

## Slide 16: Signed Integers
A signed integer can be positive or negative.
The most significant bit (MSB) is reserved for the sign:
    1 means negative and 0 means positive.
Example:
  00001010 = decimal 10
  10001010 = decimal -10

## Slide 17: One’s Complement
The one’s complement of an integer is obtained by complementing each bit, that is, replace each 0 by a 1 and each 1 by a 0.

## Slide 18: 2’s Complement
Negative integers are stored in computer using 2’s complement.
To get a two’s complement by first finding the one’s complement, and then by adding 1 to it.
Example
  11110011 (one's complement of 12)
  + 1 (decimal 1)
  11110100 (two's complement of 12)

## Slide 19: Subtract as 2’s Complement Addition
Find the difference of 12 – 5 using complementation and addition.
00000101 (decimal 5)
11111011 (2’s Complement of 5)
  00001100 (decimal 12)
  + 11111011 (decimal -5)
  00000111 (decimal 7)
No Carry

## Slide 20: Example
Find the difference of 5ABCh – 21FCh using complementation and addition.
5ABCh = 0101 1010 1011 1100
21FCh = 0010 0001 1111 1100
1101 1110 0000 0100 (2’s Complement of 21FCh)
0101 1010 1011 1100 (Binary 5ABCh)
+ 1101 1110 0000 0100 (1’s Complement of 21FCh)
10011 1000 1100 0000
Discard Carry

## Slide 21
  Binary, Decimal, and Hexadecimal Equivalents.